Digital Watchdog is a leading manufacturer of security and surveillance solutions, offering stunning image quality, advanced hardware capabilities, reliable customer support and lowest total cost of deployment to the analog & IP megapixel surveillance markets. Located in Tampa, FL with manufacturing facilities in Seoul, Korea, Digital Watchdog is committed to delivering powerful security solutions to its customers worldwide.

For additional information, contact:

# Digital Watchdog, Inc.

# 16220 Bloomfield Avenue. Cerritos,

# California USA 90703 USA

# Phone: (866) 446-3595

# Web: www.digital-watchdog.com

# E-mail:  dw-tech@digital-watchdog.com

HIGH DEFINITION OUTDOOR PTZ DOME VIDEO CAMERA

# DIVISION 28 – ELECTRONIC SAFETY AND SECURITY

2820 00 	Electronic Surveillance

28 23 00 	Video Surveillance

28 23 29	Video Surveillance Remote Devices and Sensors

Notes to Specifier:

1.  Where several alternative parameters or specifications exist, or where, the specifier has the option of inserting text, such choices are presented in <bold text>.

2.  Explanatory notes and comments are presented in colored text.

HIGH DEFINITION OUTDOOR PTZ DOME VIDEO CAMERA

- GENERAL

  - SUMMARY

    - Section includes at 2.1MP high definition PTZ video camera with outdoor rated dome housing.

    - Product - A high definition PTZ video camera, capable of transmitting 30 fps at resolutions up to1945 x 1097 video over analog connections, in a vandal resistant IP66 rated dome housing.

## Related Requirements

      - 27 20 00 Data Communications

      - 28 23 13 Video Surveillance Control and Management Systems

      - 28 23 16 Video Surveillance Monitoring and Supervisory Interfaces

      - 28 23 19 Digital Video Recorders and Analog Recording Devices

      - 28 23 23 Video Surveillance Systems Infrastructure

  - REFERENCES

    - Abbreviations

      - AGC - Automatic Gain Control

      - ARP – Address Resolution Protocol

      - AWB  - Automatic White Balance

      - BLC – Back light compression

      - DHCP - Dynamic Host Configuration Protocol

      - DNR – Digital Noise Reduction

      - DNS - Domain Name Server

      - DDNS –Dynamic Domain Name Server

      - fps - frames per second

      - FTP - File Transfer Protocol

      - GUI – Graphical User Interface

      - HLC – Highlight Compensation

      - HTTP - Hypertext Transfer Protocol

      - ICMP – Internet Control Message Protocol

      - IGMP - Internet Group Management Protocol

      - IP - Internet Protocol

      - JPEG - Joint Photographic Experts Group

      - MJPEG - Motion JPEG

      - MPEG - Moving Pictures Experts Group

      - NTP - Network Time Protocol

      - PoE - Power over Ethernet

      - PPPoE - Point-to-Point Protocol over Ethernet

      - QoS – Quality of Service

      - RARP – Reverse Address Resolution Protocol

      - RTP - Real-Time Transport Protocol

      - RTSP - Real-Time Streaming Protocol

      - SMTP - Simple Mail Transfer Protocol

      - SNMP – Simple Network Management Protocol

      - TCP - Transmission Control Protocol

      - UDP - User Datagram Protocol

      - UPnP – Universal Plug and Play

      - VMS - Video Management System

      - WDR – Wide Dynamic Range

    - Reference Standards

      - Network

        - IEEE - 802.3 Ethernet Standards

      - Video

        - ISO / IEC 14496 – MPEG-4

          - ISO / IEC 14496–10, MPEG-4 Part 10 ( ITU H.264)

        - ISO / IEC 10918 – JPEG

        - ONVIF–Profile S

      - Emissions

        - FCC-47 CFR Part 15 Class B

      - Environmental

        - ANSI / IEC60529 – Degrees of Protection Provided by Enclosures – IP66

  - SUBMITTALS

    - Product Data

      - Manufacturer’s printed or electronic data sheets

      - Manufacturer’s installation and operation manuals

      - Warranty documentation

  - QUALIFICATIONS

    - Manufacturer shall have a minimum of five years’ experience in producing IP video equipment.

    - Installers shall be trained and authorized by the Manufacturer to install, integrate, test, and commission the system.

## DELIVERY, STORAGE AND HANDLING

## Deliver the camera in the manufacturer’s original, unopened, undamaged container with identification labels intact.

## Store the camera in a temperature environment of -10° C to 50° C (14° F to 122° F), protected from mechanical and environmental conditions as designated by the manufacturer.

END OF SECTION

- PRODUCTS

  - EQUIPMENT

    - Manufacturer: 	Digital Watchdog, Inc.

16220 Bloomfield Avenue. Cerritos,

California USA 90703 USA

Phone: (866) 446-3595

Web: www.digital-watchdog.com

E-mail:  dw-tech@digital-watchdog.com

    - Model		DWC-PTZ20X

    - Alternates: None

  - GENERAL DESCRIPTION

    - The High Definition PTZ Dome Camera (“PTZ Dome camera”) shall capture and transmit 1080p, 2.1MP video over an analog connection, for the purpose of allowing users to integrate it with digital video recorder or digital video encoder products.

    - The PTZ dome camera shall possess the following characteristics:

      - 2.1 megapixels

      - day/night operation with IR cut filter

      - 16 x digital zoom, 20 x optical zoom

      - Double shutter Wide Dynamic Range

      - Wide Dynamic Range (WDR):	100 dB minimum

      - 16 privacy masking regions

      - integral motion detection

      - 3D digital noise reduction

      - alarm input and output

      - multicast or unicast capable

      - IP66 rated vandal resistant housing

  - VIDEO

    - Connection

      - The PTZ dome camera shall include the following connectors:

        - Video Output: 1 BNC (HD-Analog, HD-TVI, CVBS selectable)

          - HD-TVI: 1080 at 30fps,720p at 30/60fps

          - HD-Analog: 1080p at 30fps

          - CVBS: 720x480 at 30fps

        - Bit rate:	1.8 Mbps – 8 Mbps

        - Frame rate:	0 – 30 fps

    - Imager

      - Sensor:	1/2.8" Sony STARVIS CMOS

      - Minimum illumination

        - Color mode: 		0.35 lux (50IRE)

        - Black & white mode:	0.013 lux (50IRE)

      - Scanning - Progressive

      - Image Control Settings shall be available for:

        - Automatic white balance (AWB)

        - Exposure modes: 		automatic or manual

          - In manual exposure mode, configurable settings for:

            - brightness

            - shutter mode: 	automatic 1/30000 at 30fps, manual

automatic 1/50000 at 60fps, manual

            - digital slow shutter up to 8x to decrease shutter speed in low light

            - Backlight compensation (BLC)

            - Automatic Gain Control (AGC)

            - WDR level:		100 dB minimum

        - Day and night settings, to allow configuration for Day (color), Night (Black and White), or Automatic.

        - Frequency

        - Image sharpness

        - Chroma

        - Image mirror or flip

        - Digital noise reduction

        - Privacy zone definition, up to 16 zones

      - Lens:

        - Lens type: 4.7 ~ 94mm, Remote Auto Focus Lens

        - Optical zoom: 20x

        - Digital zoom: 16x

        - Field of view (FOV): 55.5o ~ 3o

        - Double shutter Wide Dynamic Range

        - Shutter speed: 	1/30000 at 30fps

1/50000 at 60fps

    - Motion Detection – The PTZ dome camera shall have the ability to detect motion within user defined areas of the video image.

      - Configuration settings shall be available for sensitivity and dwell time.

    - ONVIF – Video streams shall be capable of supporting ONVIF protocol, profile S.

    - Pan Tilt

      - Pan Range:	360o

      - Tilt Range:	-10 ~ 190o

      - Presets:	240

      - Tours:		up to 8

        - entries per tour:	20

      - Patterns: 	up to 8

      - Home function: 	Supported

      - Speed:		380o per second

      - Protocol:	Pelco-P, Pelco-D

    - Other

      - Alarm/Sensors – The PTZ dome camera shall have four alarm/sensor inputs and two alarm/control output.

  - ADDITIONAL FEATURES

    - Auxiliary Inputs and Outputs

      - Input: Alarm sensor (contact closure)

      - Output: Relay

  - ELECTRICAL

    - Power

      - Sources

        - 24VAC, 12VDC

      - Power Consumption:

        - Max, 1A (12W) @ 12VDC, 24VAC

      - External power (12 VDC):	2-conductor power to terminal block

      - Alarm In and Out:		up to 6 wire connection to terminal block

  - MECHANICAL AND ENVIRONMENTAL

    - Housing Material: 		aluminum housing, polycarbonate dome

    - Configuration:		PTZ dome

    - Dimensions (D x H): 	6.06 in. x 5.9 in. (154mm x 150 mm)

    - Temperature:

      - Operating:		-10° C to 50° C (14° F to 122° F)

    - Humidity:			0 - 90%, non-condensing

    - Environmental Rating:	IP66

END OF SECTION

- EXECUTION

  - INSTALLERS

    - Contractor personnel shall comply with all applicable state and local licensing requirements.

## PREPARATION

## The network design and configuration shall be verified for compatibility and performance with the camera(s). Network configuration shall be tested and qualified by the Contractor prior to camera installation.

  - INSTALLATION

    - Before permanent installation of the system, the Contractor shall test the system in conditions simulating the final installed environment

      - A report indicating successful test results shall be produced.

  - STORAGE

    - The PTZ dome camera hardwareshall be stored in an environment where temperature and humidity are in the range specified by the Manufacturer.

END OF SECTION